## Slide 1: Software Development Networking Basics
Artificial Intelligence Training
Created by Andrew Ferlitsch
Instructor Feb. 2018

## Slide 2: SOCKET
Connect – Client requests connection with Server
Accept - Server accepts (rejects) connection from Client
Send – Client (Server) sends data to Server (Client)
Recv – Server (Client) reads data sent from Client (Server)
Data Communication between Client and Server
Client
Connect
Server
Accept
Send
Data A
Recv
Data A

## Slide 3: Chunking
A message maybe broken into multiple packets.
Each packet is sent separately.
The other end reassembles the packets into the message.
Happens at the Transport Layer (invisible to you)
Data is Transmitted through a network in Packets
Client
Server
Send
Data A
Recv
Data A
Data A1
Data A2
Data A3
Data is broken into chunks,
each transmitted separately.
Chunks are reassembled into
data packet at receiving end.

## Slide 4: Packet Transmission
Packets are sent in one or more chunks from the Client.
A router identifies the route through the network to
transmit the chunks to the Server.
Packet Chunks are routed through a network for reassembly on the other end.
Router
Client
Data A
Send
Data A1
Data A2
Data A3
Server
Data A2
Data A1
Data A3
Chunks maybe sent and arrive in
a different order.
Each chunk has an ID to reassemble
in correct order on receiving end.
Data A

## Slide 5: TCP vs. UDP
UDP (User Datagram Protocol) – Sends data packets (chunks) without confirming they are received (i.e, data maybe lost at receiving end).
  Fastest Transmission – No Handshaking Required
  Choose when not a problem if some data does not
  arrive.
TCP (Transmission Control Protocol) – Sends data packets
(chunks) and receives acknowledgement they are received.
  If packet (chunk) does not arrive it resents missing data.
  Two-Way communication. Send and Receive acknowledgement.
  Sender waits for all acknowledgements to arrive over the
  network.

## Slide 6: UDP
Client sends data out in packet chunks to Server.
Client does not know if all the packet chunks arrived at
Server.
Data is sent through network using one-way transport link.
Client
Data A
Send
Data A1
Data A2
Data A3
Lost Packet
Server
Recv
Data A1
Data A3

## Slide 7: TCP
Client sends data out in packet chunks to Server.
Receiver sends acknowledgement of receipt.
If packet chunk is lost, Client resends it.
Data is sent through network using two-way transport link.
Client
Data A
Send
Data A1
Data A2
Data A3
Lost Packet
Server
Recv
Data A1
Data A3
Acknowledgement (Ack)
Resend
Data A2
Ack
Data A2

## Slide 8: Internet Addressing (IP)
Devices send/receive data through a network interface.
Devices (Hosts) on a network have a Network Address.
Host 1
Host 2
Network Interface Card (NIC)
MAC
IP Addr
Media Access Control - Universal Unique Identifier
of NIC interface.
Internet Protocol Address – Unique routing address on the Internet.
IP address is mapped to MAC address within a local area network (LAN)
IP addresses are used to route between LANs across a wide area
network (WAN), e.g., Internet.
Network Interface Card (NIC)
MAC
IP Addr
Machines connect via their IP addresses

## Slide 9: Routing
In a LAN, data is routed according to MAC address
Routers handle mapping device MAC addresses and assigning IP addresses.
Host 1
Network Interface Card (NIC)
MAC
IP Addr
Router
Registers MAC (permanent) address with router.
Router keeps table
of MAC to IP address
lookups.
Router sends back
assigned (temporary)
IP address.
Host 2
Network Interface Card (NIC)
MAC
IP Addr

## Slide 10: Subnets (C, B, A)
Routes are broken into Subnets, smallest is C-Subnet
IP Addresses are broken into subnets. Routers handle routing data within and between subnets.
Host aaa.bbb.ccc.1
Host aaa.bbb.ccc.254
Host aaa.bbb.ccc.2
Host aaa.bbb.ccc.255
Router
C-subnet address
C-subnet covers a range of 256 devices

## Slide 11: DNS Lookup
When a connection is made to a domain name alias, the
client makes a request to a Domain Name Server (DNS),
which does a lookup to return an IP address.
Domain Names are ways of giving a Name Alias to a (logical) device on a WAN
DNS Lookup
Client
Host Name
IP Address
Server
Send Host Name
of Server (e.g., google.com)
Return IP address of Server
Router
Data
Uses IP Address to
send data
Data

## Slide 12: DNS Network
Host (client) -> LAN -> ISP -> Primary Name Server
DNS Name Lookups are maintained by a distributed system of DNS Servers
DNS Lookup
Client
Local cache of
domain name to IP address
Local Area Network
DNS Server
/etc/hosts
LAN
DNS Lookup
ISP DNS Server – cached
copy of global lookups.
ISP
Primary Name Server
DNS Lookup
Master copy of global
Lookups.
Replicated across seven
Primary DNS Servers.

## Slide 13: Ports
Ports provide the logical mapping between an application and an IP address.
  64K ports per IP Address – supporting upto 64K applications.
  Reserved ports: e.g., 80 and 443 (SSL) for Internet
Ports provide mechanism for different applications to have own connection to an IP address.
Router
Client
Web Browser
FTP
Other
Data A
Data B
Data C
Port: 80
Port: 21
Port: 5000
Same IP Address
Data A
Data B
Data C
Port: 80
Port: 21
Port: 5000

## Slide 14: Client Socket
Clients connect to a Port on a Server, and then send/receive data.
function Client( host, message ) {
ipAddr = getIPAddr(host) # Convert host name (who to connect to) to IP Address
protocol = set protocol # Choice transmission protocol (TCP vs UDP)
port = set port # Choice the port that server side is listening to
connection = socket( protocol) # Create a socket configured for protocol
connection.connect( ipAddr, port) # connect to the server for the specified port
data = encode( message ) # Encode the message into byte stream for transmission
connection.send( data ) # send the data to the application on the server listening
# on this port.
response = connection.recv() # Receive response data from server.
connection.close() # Close the connection to the server
}
Connection is opened with Server
Data is sent over the network
Client waits for response (if any)

## Slide 15: Client Socket
socket.connect() – Requests for connection to Server. Will wait until server accepts or
rejects connection. Will fail if host not reachable, or no server-side application listening on the port.
socket.send() - Sends data to the Server. Non-blocking. Will return without waiting for
data to be received.
socket.recv() – Receives data from the server. Blocking, will wait until data is received. If connection is closed by server, it will unblock and return no data.
socket.close() – Closes the connection to the Server, and releases associated resources.

## Slide 16: Server Socket
Server binds to a Port on a Server, and accepts connections to send/receive data.
function Server() {
ipAddr = getIPAddr(localhost) # Convert local host name (server) to IP Address
protocol = set protocol # Choice transmission protocol (TCP vs UDP)
port = set port # Choice the port that server side will listen to
server = socket( protocol) # Create a socket configured for protocol
server.bind( ipAddr, port) # Bind to the IP address and port
server.listen() # Enable listening for a connection from client.
connection = server.accept() # Wait for a connection from a client.
request = connection.recv() # Receive request data from client.
response = process(request) # Process the request data
connection.send(response) # Send a response back to the client.
connection.close() # Close the connection to the server
}
Connection is opened on Server
Server accepts connection from a client
Server waits for data

## Slide 17: Server Socket
socket.bind() – Binds a server application to a port. Only one application can bind to a specific port.
socket.listen() – Sets up a listener process for listening for client connections on the aforementioned port.
socket.accept() – Accepts a connection from a client on the aforementioned port. Will block while waiting for a connection.
socket.recv() – Receives data from the client. Blocking, will wait until data is received. If connection is closed by client, it will unblock and return no data.
socket.send() - Sends data to the Client. Non-blocking. Will return without waiting for
data to be received.
socket.close() – Closes the connection to the Client, and releases associated resources.

## Slide 18: Echo Server
Server that echoes back to Client the message the Client sent, using a RAW protocol.
RAW Protocol means that the data is not framed inside a data package. It is sent raw with some agreed method to delineate the end of the message.
Server
Message
Client 1
Send
Send
Recv
Message
Recv

## Slide 19: Echo Server – Client Side
function EchoClient( host, message ) {
ipAddr = getIPAddr(host) # Convert host name (who to connect to) to IP Address
protocol = set protocol # Choice transmission protocol (TCP vs UDP)
port = set port # Choice the port that server side is listening to
connection = socket( protocol) # Create a socket configured for protocol
connection.connect( ipAddr, port) # connect to the server for the specified port
data = encode( message ) # Encode the message into byte stream for transmission
msglen = len(data) # Calculate the length of the message connection.send( msglen ) # Send the length of the message to the server.
connection.send( data ) # send the data to the application on the server listening
# on this port.
response = connection.recv(len(data)) # Receive response data from server.
expect( response == message ) # expect the response to equal the message sent.
connection.close() # Close the connection to the server
}
Tell the Server how long the message is
Wait for response that is the same number of bytes as the message

## Slide 20: Echo Server – Server Side
function EchoServer( ) {
ipAddr = getIPAddr(localhost) # Convert local host name (server) to IP Address
protocol = set protocol # Choice transmission protocol (TCP vs UDP)
port = set port # Choice the port that server side will listen to
server = socket( protocol) # Create a socket configured for protocol
server.bind( ipAddr, port) # Bind to the IP address and port
server.listen() # Enable listening for a connection from client.
while forever {
connection = server.accept() # Wait on a connection from a client.
msglen = connection.recv(1) # read first byte for length of message
message = connection.recv( msglen ) # receive the message
connection.send( message ) # echo the message back to the client
connection.close() # close the connection with the client }
}
Continuous process echo requests
Receive the number of expected bytes